## Slide 1: Continuous Glucose Monitoring
Education for Family Practice Employees
Fall 2023
Sarah Anderson, RN, BSN, CDCES

## Slide 2: Objectives
On completion of this program, participants should be able to:
Describe how continuous glucose monitoring (CGM) technology works, the benefits of CGM, and how it is different than blood glucose monitoring.
Identify important teaching points that should be shared with patients prior to starting CGM.
Teach patients how to start and independently use the four most commonly prescribed CGM models.

## Slide 3: Part 1 All about Continuous Glucose Monitoring (CGM)

## Slide 4: What is Continuous Glucose Monitoring?
A small metal filament inserted under the skin monitors the amount of glucose in the interstitial fluid (fluid between the fat cells).
A new reading is taken every one or five minutes, depending on the model.
This data is viewed either on an accompanying receiver or cell phone app.
FDA approved to replace fingersticks for monitoring glucose levels and making treatment decisions (such as how much insulin to take).

## Slide 5: CGM vs. Glucometer
CGM
Measures the amount of glucose in the interstitial fluid
Provides a new glucose reading every 1 or 5 minutes
Sensor stays on the body for 10 or 14 days
GLUCOMETER
Measures the amount of glucose in the blood
Provides a reading for one moment in time
Requires a drop of blood from the finger or alternate site for each reading

## Slide 6: Benefits of CGM – “Pros”
Reduced need for fingersticks – usually biggest draw for patients.
Ability to see glucose levels at all times of the day and night.
Monitors fluctuations in glucose levels caused by:
  Food choices/amounts
  Medication
  Physical activity
  Health
  Stress
High and low alarms.
  Low alarm is a safety feature.
  High alarm can alert patients if they have forgotten an insulin dose or if they have had a food/drink that spikes their glucose level.
Downloadable reports can be viewed by patients and providers (right now mostly Endo and Diabetes Ed).

## Slide 7: Benefits of CGM – “Pros”
Can promote lifestyle changes. According to one study:
  Ninety percent of continuous glucose monitoring (CGM) users felt that its use contributed to a healthier lifestyle.
  Forty-seven percent of CGM users reported being more likely to go for a walk or do physical activity if they saw a rise in their blood glucose.
  Eighty-seven percent of CGM users felt that they modified their food choices based on CGM use.
  Source: Ehrhardt N, Al Zaghal E. Continuous Glucose Monitoring as a Behavior Modification Tool. American Diabetes Association Clin Diabetes 2020 Apr; 38(2): 126-131

## Slide 8: Potential Drawbacks of CGM – “Cons”
Data can be overwhelming or overstimulating – “always on”.
Sensors do sometimes fail or fall off early.
  Customer service will replace free-of-charge, however this can be cumbersome and time consuming for patients if happens frequently.
Information can be misleading if sensor fails.
  Safety issue if not caught by the patient.
    A failed sensor could cause the reading on the receiver to drop to and stay at 40 mg/dl, which could cause the patient to treat a false low.

## Slide 9: Part 2 Teaching Patients about CGM

## Slide 10: Terms
Sensor - the device that is applied to the body; a small metal filament under the skin senses the glucose levels in the interstitial fluid. This is NOT a needle.
  Libre sensors last 14 days.
  Dexcom sensors last 10 days.
Transmitter - (Dexcom G6 only) – sends, or transmits, the glucose information from the sensor to the receiver.
  The Dexcom G6 transmitter lasts for 90 days.
  There is no separate transmitter in the other models. The sensor and transmitter are combined in the Dexcom G7, Libre 2 and Libre 3.
Receiver - device that receives the glucose readings from the sensor.
  Available for all models, however Libre 3 receiver is only available to people with Medicare.

## Slide 11: What to Teach Patients – All CGM Models
Always test with a glucometer with any low glucose readings, hypoglycemia symptoms, or if the reading on the sensor is higher or lower than expected.
  Make sure that patients have glucometer supplies as a back up.
  If a sensor fails, the reading on the receiver/app could drop to 40 mg/dl, no matter the actual glucose level.
Sensor information lags behind glucometer information by 10-15 minutes.
  Sensor readings do not usually match glucometer readings exactly, and readings will be further apart if BG is checked when glucose level is rising or falling quickly.
  Picture the glucometer reading as the “engine” of a train, and sensor reading as the “caboose”.

## Slide 12: What to Teach Patients – All CGM Models
All available models have customizable high and low alarms.
  Most important during initial teaching is the low alarm, which is pre-set to 70 mg/dl.
  Can adjust per patient preference, however we generally don’t recommend setting the low alarm below 70 mg/dl.
  There is an urgent low setting on all devices which is set to 55 mg/dl. This cannot be changed or turned off.
  High alarm is pre-set to 240 mg/dl or 250 mg/dl, depending on the model. Can change per patient preference.
If a sensor falls off early or stops working, do not throw it away! Contact Dexcom or Freestyle customer service. They will usually send a replacement free-of-charge.
  Do not contact VMG or the pharmacy – not able to replace.

## Slide 13: What to Teach Patients – All CGM Models
All models allow for calibration if glucometer and sensor readings are different. This is not required, but helps with accuracy.
Sensors are waterproof – can be worn in the shower, bath, and while swimming.
Over-patches are available OTC if patients have trouble with sensors not staying on for the full 10 or 14 days.
Sensor insertion device contains a needle and needs to be disposed of in a sharps container.

## Slide 14: Part 3 Getting Patients Started on CGM – The 4 Most Common Models

## Slide 15: Dexcom G6
Requires sensors, transmitter, and receiver or cell phone app. Make sure Bluetooth is enabled if using phone app.
Sensors are changed every 10 days.
Transmitter is changed every 90 days.
Follow the prompts on the receiver and the instruction sheet provided with each sensor to do the following:
  Basic set-up in the receiver or app. App will require patients to create an account with a valid email address.
  Choose insertion site (abdomen or back of upper arm), and clean with alcohol wipe.
  Enter transmitter serial number into the receiver/app.
  Enter sensor serial number into the receiver/app.
  Insert sensor into the abdomen or back of upper arm.
  Attach transmitter. Listen for 2 clicks to ensure it is fully engaged.
  Go back to receiver/app and tap start sensor.
  Transmitter pairing and 2 hour sensor warm-up period will begin.

## Slide 16: Dexcom G7
Requires sensors and receiver or cell phone app. Make sure Bluetooth is enabled if using phone app.
Sensors are changed every 10 days, with a 12 hours “grace period”.
Follow the prompts on the receiver and the instruction sheet provided with each sensor to do the following:
  Basic set-up in the receiver or app. App will require patients to create an account with a valid email address.
  Choose insertion site (abdomen or back of upper arm), and clean with alcohol wipe.
  Insert sensor into the abdomen or back of upper arm.
  Enter the 4-digit sensor serial number.
  Go back to receiver/app and tap start sensor.
  30-minute warm-up period will begin.

## Slide 17: Freestyle Libre 2
Requires sensors and receiver or cell phone app. Make sure Bluetooth is enabled if using phone app.
Sensors are changed every 14 days.
Follow the prompts on the receiver and the instruction sheet provided with each sensor to do the following:
  Basic set-up in the receiver or app. App will require patients to create an account with a valid email address.
  Choose insertion site (back of R or L upper arm), and clean with alcohol wipe.
  Insert sensor.
  Tap “Start New Sensor” on app or receiver and scan the sensor.
  60-miunute warm-up period will begin.
IMPORTANT: teach patients to scan the sensor each time they want to know their glucose level, it will not auto-populate. To avoid losing data, do not go longer than 8 hours without scanning the sensor.

## Slide 18: Freestyle Libre 3
Requires sensors and receiver or cell phone app. Make sure Bluetooth is enabled if using phone app.
Sensors are changed every 14 days.
Follow the prompts on the receiver and the instruction sheet provided with each sensor to do the following:
  Basic set-up in the receiver or app. App will require patients to create an account with a valid email address.
  Choose insertion site (back of R or L upper arm), and clean with alcohol wipe.
  Insert sensor.
  Tap “Start New Sensor” on app or receiver and scan the sensor.
  60-miunute warm-up period will begin.
Does not require scanning, patients can simply look at the receiver or app when they want to know their glucose levels.

## Slide 19: Changing the Sensor
The receiver or app will notify the patient when the sensor needs to be changed.
After the 10 or 14 days, the sensors can be taken off like a band-aid and thrown in the trash. They are not sharps, because the metal filament is not a needle.
  IMPORTANT: If patients are using the Dexcom G6, they need to separate the transmitter from the sensor before throwing the sensor away. The transmitter is reusable for 90 days, or through 9 sensors.
Follow the prompts on the receiver or app to stop the old sensor, enter a new sensor serial number and apply the new sensor.
  If using Dexcom G6, patients do not have to enter the transmitter SN every time.

## Slide 20: Follow-up/When to Contact VMG
Patients should follow-up with their providers as recommended.
Follow-up with Diabetes Education as needed or recommended by PCP.
  Not all patients will need to be seen by Diabetes Education. Would be recommended if patients could benefit from a review of their CGM report for insulin titration or medication changes.
Remind patients not to contact VMG or their pharmacy if sensor stops working or falls off early. They should contact Dexcom or Freestyle customer service for a replacement.

## Slide 21: Questions?
Thank you for attending!
How to contact Diabetes Education:
Sarah Anderson
sanderson@vmgma.com
Athena text/Patient case
(413) 256-4468